## Slide 1: CPE 133
Number Systems Conversions
Useful Codes
Digital Design Problem

## Slide 2: Important Information
Friday: the first lab
  Laptop users:
  download Xilinx Vivado 18.2 WebPack
  Not enough benches for everyone
The course in general
  Starts slow picks up when labs start
  When labs start, you’re learning digital design and Verilog simultaneously
Don’t let the initial slow pace fool you

## Slide 3: Number Systems Conversions
Any radix to decimal
  1011.112 to decimal
  4AF.2D16 to decimal
Binary ↔ Hexadecimal
  11000101001.110012 to hexadecimal
  3AF8.2D16 to binary

## Slide 4: “Binary” Multiplication & Division
Multiply 23A.4716 by 256
Divide DEAD.BEEF16 by 16
Multiply 10011101.112 by 32
Divide 100011.11012 by 16

## Slide 5: Useful Codes
Binary Coded Decimal (BCD)
  367 to BCD
  001101101001BCD to decimal
One-hot codes
  Number of bits = number of codewords
  Only one bit set in each codeword
Unit Distance Codes
  Distance: quantity of bits you need to change to go from one codeword to another codeword
  Often referred to as “gray codes”

## Slide 6: Digital Design and Modeling
Digital design two main qualities:
  Modular
  Hierarchical
Definition 1: A representation of something
Definition 2: A description of something in terms that highlights the relevant information while hiding the less useful information
Purpose: transfers information to the entity reading the model
Comments:
  No absolutely “correct” model

## Slide 7: Digital Design Description
An approach to digital design:
  Define the problem: understand the starting point and requirements
  Describe your solution to the problem: propose your path to the solution
  Implement your solution to the problem: embodiment of the solution
Main Design approaches:
  BFD – brute force design (iterative design)
  IMD – iterative modular design
  MD – modular design

## Slide 8: Digital Design Description
A typical design approach:
  Define the problem: understand the starting point and requirements
  Describe your solution to the problem: propose a path to the solution
  Implement your solution to the problem: embodiment of the solution
Example: Problem Statement - Design a digital circuit where the output of the circuit indicates when the 3-bit binary number on the input is greater than four. State how your circuit is controlled.

## Slide 9: The First Steps in Solution
Define the high-level interface: draw a high-level black box diagram (BBD)
  box has name
  inputs and outputs clearly marked
  annotations clarify the diagram
Design on design approach
  brute force design (BFD)

## Slide 10: Step 1: Define the Problem
The BFD thing

## Slide 11: Step 2: Describe your Solution
Algebra: a mathematical system used to generalize arithmetic operations by using letter or symbols to stand for numbers based on rules derived from a minimal set of basic assumptions
Axioms: a set of basic assumptions that are universally accepted as true.
Theorems: propositions that can be proved true using basic axioms
George Boole: created a two-valued algebra (Boolean Algebra)
  Based on a set of operators defined over a set of elements in question.
  Elements are: {0,1}
  Operators are: defined by axioms

## Slide 12: Basic Axioms of Boolean Algebra
operators and numbers…

## Slide 13: Basic Boolean Algebra Operators
Truth tables for basic logic functions

## Slide 14: Boolean Algebra Theorems

## Slide 15: Three Solution Descriptions
Written Description
Tabular Description:
Truth Table
Boolean Algebra Description

## Slide 16: Step 3: Implement your Solution
Pretend you’re really going to build this circuit…

## Slide 17: Basic Boolean Operators and Gates
Gates: Implement basic Logic Functions

## Slide 18: The Circuit Solution
Create circuit by using gates to represent logic operations
Boolean Algebra Description
Circuit Model of Solution

## Slide 19: Four Equivalent Solution Descriptions
Written Description
Tabular Description
Boolean Algebra Description
Circuit Description

## Slide 20: Example Problem
Design a circuit whose 3-bit output is two greater than the 3-bit input. Outputs that exceed the 3-bit range should be set to zero.
  Provide Boolean equations describing output
  Provide circuit diagram using AND gates, OR gates, and inverters

## Slide 21: Example Problem
Write a Boolean equation describing the following circuit.