## Slide 1: CPE 133
Experiment 1 Overview
New Gates
Function Forms
Experiment 2 Introduction

## Slide 2: Experiment #1: The Point
What you did:
  Designed, modeled, and implemented standard digital circuit on an FPGA
  Used Boolean equations to define outputs in terms of inputs
How you did it:
  Used the Vivado design tools suite
    Xilinx Design Methodology
How you tested your design:
  You did a visual test

## Slide 3: Function Representations
Standard Sum of Products (SOP)
  Write an expression for the 1’s
Standard Product of Sums (POS)
  Write an expression for the 0’s
  DeMorganize it
Minterm: product term containing all independent variables of the function
Maxterm: sum term containing all independent variables of the function
  Maxterm = !(Minterm)
  Minterm = !(Maxterm)
Functional Equivalence

## Slide 4: Representing Functions
Standard SOP & POS (equations)
Compact minterm & Compact maxterm
Circuit form (schematic)
Truth table
You should be able to go from any one form to any other form

## Slide 5: New Gates
NAND Gate
NOR Gate
XOR
XNOR
Functionally Complete
Functionally Complete

## Slide 6: Circuit Forms
Many Different circuit forms
  We’ve worked with about 10 of them
  “circuit forms” refers to basic implementation styles
    Some styles are more useful than others
Styles you’re used to:
  AND/OR (SOP)
  OR/AND (POS)
Standard circuit forms come from SOP and POS forms and applications of DeMorgan’s theorems

## Slide 7: DeMorgan’s Theorem
General form
Most used theorem in digital design

## Slide 8: Example: the 8 Standard Circuit Forms
F(A,B,C) = SUM(0,1,7)

## Slide 9: Drawing NAND/NAND & NOR/NOR Circuits
AND/OR
Bad NAND/NAND
Good NAND/NAND
OR/AND
Bad NOR/NOR
Good NOR/NOR

## Slide 10: HDL Thoughts
HDL: Hardware Description Language
  presents an unambiguous way to model digital circuits
  models allow for the circuit simulations
  Verilog supports hierarchical modeling
  Verilog models can be used to generate actual circuits
Verlog is not:
  VHDL is not a programming language
    as the name states, it’s a description language
  Bad at and/or dislike programming?
    You’re modeling digital circuit

## Slide 11: VHDL Invariants
Case Sensitivity:
  case sensitive
White space:
  white space is ignored
Comments:
  anything after a “// “ (two slashes) is ignored
  “block” comments /* */ (multiline comment)
Parenthesis:
  few requirements; use for code clarity
  operator precedence??

## Slide 12: Example
Implement the following function:
module my_ckt (A,B,C,D,F);
input A,B,C,D;
output F;
assign F = (A & ~B) | (C & ~D);
endmodule

## Slide 13: Verilog & Concurrency
Higher-level Language
A = B + C;
D = E + F;
G = H + I;
VHDL
assign A = B & C;
assign D = E & F;
assign G = H & I;

## Slide 14: 2 Types of Concurrent Statements
Continuous Assignment
always blocks
Notes: This is a list of the four major types of concurrent statements used in VHDL. The previous example showed concurrent signal assignment. This set of slides talks about the first three. The next set of slides will talk about process statements.

## Slide 15: Operators
AND: &
  Example: A & B
OR: |
  Example: A | B
Inversion: ~
  Example: ~A
NAND: ~(A & B)
NOR: ~(A | B)

## Slide 16: Experiment #2: Full Adder (FA)
Full Adder in SOP & POS forms
  Assignment B only
Objectives: to prove SOP and POS forms are functionally equivalent
Use any switches and LEDs you want
Lab Submissions
  Not a “lab report”
  Read the Lab Manual for details
  Don’t ever submit constraints file