## Slide 1: CPE 133
More Verilog Details
Structural Modeling
Ripple Carry Adders
Experiment #3

## Slide 2: Verilog Data Types
Scalar quantities
Vector quantities
module my_ckt (A,B,C,D,F);
input A,B,C,D;
output F;
assign F = (A & ~B) | (C & ~D);
endmodule
module my_ckt (A,B,C,D,F);
input [3:0] A,B,C,D;
output [3:0] F;
assign F = (A & ~B) | (C & ~D);
endmodule

## Slide 3: Example: entity declarations
module my_ckt1 (A,B,C,F1,F2);
input A,B,C;
output F1,F2;
//- statements
endmodule
module my_ckt2 (D,G,H,F3,F4);
input [1:0] D,G;
input H;
output [3:0] F3,F4;
//- statements
endmodule

## Slide 4: Digital Design Issues
An approach to digital design:
  Define the problem: understand the starting point and requirements
  Describe your solution to the problem: propose your path to the solution
  Implement your solution to the problem: embodiment of the solution
Main Design approaches:
  BFD – brute force design (iterative design)
  IMD – iterative modular design
  MD – modular design

## Slide 5: 4-bit Ripple Carry Adder
Implement using Verilog Structural Modeling
  Use at least two-levels in your design
  Use bundle notation (not individual signals)
  Don’t simulate

## Slide 6: RCA Foundation Module
RCA Foundation Module Notation
Generic Digital Circuit

## Slide 7: Experiment 3: 5-bit Ripple Carry Adder
Make it incredibly neat and organized
  Indentation provides information
This is true digital modeling (hierarchical)
Verilog structural modeling
  Initially syntactical pain in the @#%$
Use bundles (buses) whenever you can
  Inputs operands & Sum output
  Internal signals?

## Slide 8: Verilog Structural Modeling
Supports hierarchical design
  Boxes within boxes
  the only way to understand and/or implement a complex digital circuit
Similar approach to good programming
  module reuse
  functional hierarchy

## Slide 9: 3-Bit Comparator

## Slide 10
//- defintion of XNOR gate
module my_xnor(A, B, F);
input A,B;
output F;
assign F = ~(A ^ B);
endmodule
//- definition of 3-input AND gate
module my_and(A, B, C, F);
input A, B, C;
output F;
assign F = A & B & C;
endmodule

## Slide 11
//- defintion of XNOR gate
module my_xnor(A, B, F);
input A,B;
output F;
assign F = ~(A ^ B);
endmodule
//- definition of 3-input AND gate
module my_and(A, B, C, F);
input A, B, C;
output F;
assign F = A & B & C;
endmodule
//- definition of 3-bit comparator
module comp_3b(A,B,EQ);
//- external interface signals
input [2:0] A,B;
output EQ;
//- internal interface signals
wire [2:0] m;
//- XNOR instantiations
my_xnor XNOR2 (
.A (A[2]),
.B (B[2]),
.F (m[2]) );
//- XNOR instantiation
my_xnor XNOR1 (
.A (A[1]), .B (B[1]), .F (m[1]) );
//- XNOR instantiation
my_xnor XNOR0 (
.A (A[0]), .B (B[0]), .F (m[0]) );
//- AND instantiation
my_and AND0 (
.A (m[2]), .B (m[1]), .C (m[0]), .F (EQ) );
endmodule