## Slide 1: CPE 133
Verilog Procedural Blocks
Standard & Non-standard decoders
Experiment 4

## Slide 2: Digital Design
It’s not about implementing functions
  K-maps to reduce functions
  No one really reduces anything any more
Following examples
  Mostly there for reference
How to learn Verilog
  Read about it, use it, ask questions, repeart

## Slide 3: Standard vs. Non-Standard Decoder
Non-standard decoder = generic decoder
Decoders: anything you can define in tabular format (table)
  Analogous to LUTs (look-up table) in programming
Standard decoder is specialized form of generic decoder

## Slide 4: Standard Decoder
Relatively simple circuit

## Slide 5: Standard Decoder Overview
Have fixed output
  One-hot (or one-cold)
Often referred to as a DMUX?
Has a somewhat specialized purpose
  Used to enable one device while disabling many other devices
General Forms: binary relationship
  1:2, 2:4, 3:8, 4:16, etc.
  Simple to model in Verilog

## Slide 6: Generic Decoders
Truth table = LUT (look up table)
  Generic decoder: LUT
Everything we’ve done was from a truth table
  Could have been implemented as a non-standard decoder
Generic Decoders: smart functions implementation
  No reduction necessary!
  Great for multiple input/multiple output modules
An initial step in any digital design is to think of a way you can implement your circuit using a LUT
  Typically: implement logic using decoder

## Slide 7: RCA Foundation Module
Standard Decoder Foundation Module Notation
Generic Digital Circuit

## Slide 8: Generic Decoder Foundation Module
Generic Decoder Foundation Module Notation
Generic Digital Circuit

## Slide 9: Verilog: Behavioral Modeling
Continuous assignment statements
  dataflow? (low level descriptions)
  Example:
    assign F = (A & ~B) | (C & ~D);
always blocks
  One type of procedural block
  Allows for modeling of circuits using a description rather than low-level logic

## Slide 10: always block Overview
Contains two types of items
  procedural assignment statements
    Example: A = B;
  procedural programming statements
    if-else statements
    case statements
All assignments must be to variables
  We only use reg types variable
    Example: A = B; //- A must be reg-type

## Slide 11: The always block
Sensitivity list
  List of every input to block
Statements
  Procedural programming
  Procedural assignment
always @(sensitivity_list)
begin : block_name
statements
end

## Slide 12: Variable Assignment
All assignments must be to reg-types
//---------------------------
//- reg declaration when
//- variable is part
//- of module interface
//----------------------------
module var_example_1(A,B,C,F);
//- external interface
input A, B, C;
output reg F;
//----------------------------
//- reg declaration when
//- variable is an
//- internal signal
//---------------------------
module var_example_2(A,B,C,F);
//- external interface
input A, B, C;
output F;
reg my_var;

## Slide 13: The if: (Procedural Programming Statements)
All assignments must be to reg-types
//--------------------------
//- not for combinatorial
//- circuits
//--------------------------
if (expression)
statement
//---------------------------
//- not for combinatorial
//- circuits
//---------------------------
if (expression)
begin
statement(s)
end

## Slide 14: The if-else: (Procedural Programming Statements)
All assignments must be to reg-types
if (expression)
statement
else //- catch-all
statement
if (expression)
begin
statement(s)
end
else //- catch-all
begin
statement(s)
end

## Slide 15: The case: (Procedural Programming Statements)
All assignments must be to reg-types
Special form of if-else statement
case (expression)
case_item : statement;
case_item : statement;
default : statement; //- catchall
endcase

## Slide 16: Representing Integers

## Slide 17: Concatenating Signals
sd

## Slide 18: Equality Operators
If “expression” arguments

## Slide 19: Example 1
What you’ve been doing

## Slide 20: Solution
module dcdr_generic_ex1(A, B, C, F);
input A, B, C;
output reg F;
//- declare bundle
wire [2:0] ABC;
//- create bundled signal with concatenation
assign ABC = {A,B,C};
always @(ABC)
begin
if (ABC == 3'b001) F = 1'b1;
else if (ABC == 3'b110) F = 1'b1;
else if (ABC == 3'b111) F = 1'b1;
else F = 1'b0; //- catch-all
end
endmodule

## Slide 21: Solution
module dcdr_generic_ex1b(A, B, C, F);
input A, B, C;
output reg F;
//- declare bundle
wire [2:0] ABC;
//- create bundled signal with concatenation
assign ABC = {A,B,C};
always @(ABC)
begin
case (ABC)
3'b001 : F = 1'b1;
3'b110 : F = 1'b1;
3'b111 : F = 1'b1;
default : F = 1'b0;
endcase
end
endmodule

## Slide 22: Example 2

## Slide 23: Solution
module dcdr_ex2a(ABCD, T123);
input [3:0] ABCD;
output reg [2:0] T123;
always @(ABCD)
begin
if (ABCD == 0) T123 = 3'b110;
else if (ABCD == 1) T123 = 3'b000;
else if (ABCD == 2) T123 = 3'b100;
else if (ABCD == 3) T123 = 3'b010;
else if (ABCD == 4) T123 = 3'b000;
else if (ABCD == 5) T123 = 3'b101;
else if (ABCD == 6) T123 = 3'b000;
else if (ABCD == 7) T123 = 3'b101;
else if (ABCD == 8) T123 = 3'b010;
else T123 = 3'b000;
end
endmodule

## Slide 24: Solution
module dcdr_ex2b(ABCD, T123);
input [3:0] ABCD;
output reg [2:0] T123;
always @(ABCD)
begin
case (ABCD)
0 : T123 = 3'b110;
1 : T123 = 3'b000;
2 : T123 = 3'b100;
3 : T123 = 3'b010;
4 : T123 = 3'b000;
5 : T123 = 3'b101;
6 : T123 = 3'b000;
7 : T123 = 3'b101;
8 : T123 = 3'b010;
default : T123 = 3'b000;
endcase
end
endmodule

## Slide 25: Common Anode Configuration
Each segment required at least two signals to make it light up

## Slide 26: Seven-Segment Displays

## Slide 27: Exp #4: BCD-to-7Segment Decoder
Four switches provide BCD
Output result on 7-segment display device
Anodes & Cathodes are active low (zero actuates)
9 signals required to actuate a single 7-segment display
  Eight signals for the segments & DP (cathodes)
  One signal to enable the display (anodes)
Work from the examples in book or PPTs
  There are several approaches to modeling this device
  Implement this device as LUT
Visually test circuit on the development board