## Slide 1: CPE 133
Review
Design Approaches: Modular Design
New Device: Multiplexors

## Slide 2: Important Comment
BBD = black box diagram
  Include for every experiment
  Include top two levels (unless specified otherwise)
Verilog Code
  Start commenting code
  Use proper header (the one given)
    Names
    Description of file
Answering Questions
  Always try to draw diagram

## Slide 3: Concurrency
Major aspect of HDL modeling
  It’s hardware design
  Hardware is inherently parallel
Behavioral modeling
  Continuous assignment
    Use for gate-level modeling
  Always blocks
    Describes functionality of circuit

## Slide 4: All I know about Digital Design
Digital design is based on a relatively small set of digital devices.
Digital design relies heavily on various modeling approaches
Digital design modeling relies heavily on hierarchical modeling

## Slide 5: Digital Design Foundation Modeling (DDFM)
Digital Design: using digital circuits to solve problems
Digital Circuit: a set of modules that exchange information under the control of “something”
Structured Design: any digital circuit can be built using a set of “foundation modules”
Foundation Modules:
  Simple to understand at a high-level
  Categorized as either a “controlled” or “controller” circuit
Four Ways to Control a Circuit: 1) none, 2) internal, 3) external, and 4) circuit
Three Design Approaches:
  Brute Force (BFD),
  Iterative Modular (IMD),
  Modular (MD)

## Slide 6: The Big Digital Design Picture

## Slide 7: Foundation Modules (thus far)
RCA
Generic Decoder
Standard Decoder

## Slide 8: Standard Decoder
Only one AND gate at a time is non-dead
Outputs 1-hot code

## Slide 9: 4:1 Multiplexor (MUX)
Alive AND gate “passes” Dx input value to output F
Dead AND gates do not affect F output as they provide ‘0’s to the output OR gate
S1 & S0 inputs “select” which D input will appear on F output

## Slide 10: MUX Overview
MUX is a “selector” circuit
  selects one of many inputs to the MUX to appear on the output of the MUX
General Forms: Binary Relationship
  2:1, 4:1, 8:1, 16:1, etc.
Straight-forward to model in VHDL
  Can select between single signals or bundles
Any design that “chooses” or “selects” between several “things” uses a MUX

## Slide 11: MUX Foundation Module
4:1 MUX

## Slide 12: MUX Example

## Slide 13: Verilog MUX Models
module mux_4t1_a(SEL, D, F);
input [1:0] SEL;
input [3:0] D;
output reg F;
always @(SEL, D)
begin
if (SEL == 0) F = D[0];
else if (SEL == 1) F = D[1];
else if (SEL == 2) F = D[2];
else if (SEL == 3) F = D[3];
else F = 0;
end
endmodule

## Slide 14: Verilog MUX Models
module mux_4t1_b(SEL, D, F);
input [1:0] SEL;
input [3:0] D;
output reg F;
always @(SEL, D)
case (SEL)
0: F = D[0];
1: F = D[1];
2: F = D[2];
3: F = D[3];
default F = 0;
endcase
endmodule

## Slide 15: Verilog 4:1 MUX Model
module mux_4t1_d(SEL, AW, AX, AY, AZ, F);
input [1:0] SEL;
input [7:0] AW, AX, AY, AZ;
output reg [7:0] F;
always @(SEL, AW, AX, AY, AZ)
case (SEL)
0: F = AW;
1: F = AX;
2: F = AY;
3: F = AZ;
default F = 0;
endcase
endmodule

## Slide 16: Modular Design
Three Steps
  0) Read and understand the problem
  1) Draw the high-level block diagram
    One block with all inputs and outputs
      From problem statement
  2) Draw the lower-level block diagram
    As many blocks as you need
      From problem statement
  3) Connect the interior blocks as required
If you use a non-standard digital device, you need to provided a complete description of it
  Define decoders with table

## Slide 17: Design Example 1:
Design a circuit that adds two 8-bit unsigned binary inputs and provides an 8-bit output. If the result of the addition is valid, the circuit output the sum as an 8-bit unsigned value; otherwise, the circuit outputs zero.
  Provide two levels of BBDs
  State how circuit is controlled

## Slide 18: Design Example 2:
Design a circuit that adds two 8-bit signed binary inputs. If the result of the addition is valid, the circuit output the sum as an 8-bit signed binary value; otherwise, the circuit outputs zero. All inputs and outputs are in RC format.
  Provide two levels of BBDs
  State how circuit is controlled

## Slide 19: Design Example 3:
Design a circuit that has two 8-bit unsigned binary inputs A & B, and one 8-bit unsigned binary output F1. The circuit adds A+B.
  If the button input is not pressed, the circuit always outputs the sum of A+B.
  If the button is pressed, the circuit outputs A+B if the 8-bit output is valid, or outputs zero otherwise.
  Provide two levels of BBDs
  State how circuit is controlled

## Slide 20: Design Problem Example 4
Design a circuit that has two 8-bit unsigned binary inputs A & B. If the sum of A+B is less than 127, the circuit outputs A; otherwise the circuit outputs B. Assume the result of the addition is always valid.
  Show top two levels of BBD
  State how circuit is controlled