## Slide 1: CPE 133
Review
Comparators
Experiment #5 Overview

## Slide 2: Design Problem Example 4
Design a circuit that has two 8-bit unsigned binary inputs A & B. If the sum of A+B is less than 128, the circuit outputs A; otherwise the circuit outputs B. Assume the result of the addition is always valid.
  Show top two levels of BBD
  State how circuit is controlled

## Slide 3: Foundation Modules (thus far)
RCA
Generic Decoder
Standard Decoder
4:1 MUX

## Slide 4: Behavioral Models: Process Statements
Behavioral Model
  Describe a circuit using statements rather than logic
  Once again free from writing Boolean equations
Always blocks
  Contain two type of statement
    Procedural assignment statements
    Procedural programming statement
      if-else & case statement

## Slide 5: Comparators
Standard digital circuit
  Classic & well-known XOR circuit
  Easy HDL behavioral modeling
Design a circuit that compares the values of two 2-bit inputs and indicates when the input values are equal

## Slide 6: Design for 2-Bit Comparator
Implied “unsigned binary”

## Slide 7: PPT Design
The classic “equivalence gate” (XNOR)

## Slide 8: 10-Bit Comparator Verilog Model
module comp_10(a, b, eq, lt, gt);
input [9:0] a,b;
output reg eq, lt, gt;
always @ (a,b)
begin
if (a == b)
begin
eq = 1; lt = 0; gt = 0;
end
else if (a > b)
begin
eq = 0; lt = 0; gt = 1;
end
else if (a < b)
begin
eq = 0; lt = 1; gt = 0;
end
else
begin
eq = 0; lt = 0; gt = 0;
end
end //- always
endmodule

## Slide 9: n-Bit Comparator Verilog Model
module comp_nb(a, b, eq, lt, gt);
input [n-1:0] a, b;
output reg eq, lt, gt;
//- default input data width
parameter n = 8;
always @ (a,b)
begin
if (a == b)
begin
eq = 1; lt = 0; gt = 0;
end
else if (a > b)
begin
eq = 0; lt = 0; gt = 1;
end
else if (a < b)
begin
eq = 0; lt = 1; gt = 0;
end
else
begin
eq = 0; lt = 0; gt = 0;
end
end
endmodule

## Slide 10: Comparator Foundation Modules
Comparator

## Slide 11: Example
Provide a Verilog structural model for a 12-bit comparator by instantiating an 8-bit and a 4-bit comparator using the n-bit comparator model. This comparator only has an EQ output.

## Slide 12: Solution
module comp_12b(a, b, eq);
input [11:0] a,b;
output eq;
wire eq4,eq8;
assign eq = eq4 & eq8;
//- instantiate 4-bit comparator
comp_nb #(.n(4)) MY_COMP4 (
.a (a[3:0]),
.b (b[3:0]),
.eq (eq4),
.gt () ,
.lt () );
//- instantiate 8-bit comparator
comp_nb MY_COMP8 (
.a (a[11:4]),
.b (b[11:4]),
.eq (eq8),
.gt (),
.lt () );
endmodule
module comp_nb(a, b, eq, lt, gt);
input [n-1:0] a, b;
output reg eq, lt, gt;
//- default input data width
parameter n = 8;
always @ (a,b)
begin
if (a == b)
begin
eq = 1; lt = 0; gt = 0;
end
else if (a > b)
begin
eq = 0; lt = 0; gt = 1;
end
else if (a < b)
begin
eq = 0; lt = 1; gt = 0;
end
else
begin
eq = 0; lt = 0; gt = 0;
end
end
endmodule

## Slide 13: Experiment 5: 8-bit Comparator with using Structural Modeling
Construct 8-bit Comparator using two 4-bit comparators
  Not efficient, but good structural model practice
Final model: two 4-bit comparators with some “extra logic” to handle EQ, GT, & LT
Use provided comparator template
Top-level Model
Lower-level Module

## Slide 14: Verilog Testbenches
Verilog model that tests your model by providing test data inputs
  Not my strong point (use cheatsheet)
  Test data = test vectors
  DUT = device under test
Call someone over to show you basic operation of simulator

## Slide 15: Testbench Overview
Stimulus driver provide test vector input to DUT
Testbench model has no inputs or outputs

## Slide 16: Testbench for 4-bit Comparator
module tb_comp_4b( );
//- stimulus connections to DUT
reg [3:0] a, b; //- stimulus outputs
wire eq, lt, gt; //- DUT outputs
//- DUT instantiation
comp_4b MY_COMP (
.a (a),
.b (b),
.eq (eq),
.lt (lt),
.gt (gt) );
initial
begin
//- initial values of a & b
a = 'hA;
b = 'hB;
//- a & b values 20 time units later
#20 a = 'hB;
b = 'hB;
//- a & b values 20 time units later
#20 a = 4'b1011;
b = 4'b0001;
//- a & b values 20 time units later
#20 a = 4'b0001;
b = 4'b0001;
end
endmodule
module comp_4b(a, b, eq, lt, gt);
input [3:0] a,b;
output reg eq, lt, gt;
always @ (a,b)
begin
if (a == b)
begin
eq = 1; lt = 0; gt = 0;
end
else if (a > b)
begin
eq = 0; lt = 0; gt = 1;
end
else if (a < b)
begin
eq = 0; lt = 1; gt = 0; end
else
begin
eq = 0; lt = 0; gt = 0;
end
end
endmodule

## Slide 17: Foundation Modules (thus far)
RCA
Generic Decoder
Standard Decoder
4:1 MUX
Comparator

## Slide 18: Design Example 1:
Design a circuit that compares three 10-bit unsigned binary values. If all three 10-bit values are equivalent, the EQ3 output of the circuit will be a ‘1’, otherwise it will be a ‘0’.
  Provide two levels of BBDs
  State how circuit is controlled

## Slide 19: Design Example #2
Design a circuit that has two unsigned binary 8-bit inputs and two 8-bit unsigned binary outputs HI & LO. The circuit outputs the greater of the two inputs values to the HI output and the other value to the low input.
  Provide two levels of BBDs
  State how circuit is controlled

## Slide 20: Design Example #3:
Design a circuit that has two 8-bit unsigned binary inputs A and B, and one 8-bit unsigned binary output F1. The greater of two input values appears on the outputs. Output either input value if the numbers are equivalent.
  Provide two levels of BBDs
  State how circuit is controlled

## Slide 21: Design Example #4
Design a circuit that has two unsigned binary 8-bit inputs and two 8-bit unsigned binary outputs X & Y. If a button is pressed, the circuit sorts in descending order (X=hi, Y=lo); otherwise the circuit sorts in ascending order (X=lo, Y=hi).
  Provide two levels of BBDs
  State how circuit is controlled