## Slide 1: CPE 133
Mixed Logic

## Slide 2: EE Department Corporate Sponsor
www.bailbondsabc.com

## Slide 3: Verilog Overview
Uses
  Modeling digital circuits
  Testing digital circuits
    Stimulus driver/checker
Amazing Language
  CPE 133 uses small basic subset
  You must understand “the basics”
    You know about 2/3 of “the basics” already

## Slide 4: Generic Digital Circuit Model
Boxes exchanging information with boxes under the control of “something”
  Nothing
  Another box (internal)
  An external signal (switch)
  Another box (FSM or MCU)

## Slide 5: Verilog Modeling
Boxes
  Continuous assignment statements
  Instantiations
  Procedural blocks (always blocks)
Connections between boxes
  Net data types
    Wire (for continuous assignment statements)
  Variable data types
    Reg (for assignments in always blocks

## Slide 6: Always blocks
Sensitivity list
  List of signals the cause evaluation of block
  Put all block inputs in sensitivity list
Statement group
  Everything between the begin & end
    Procedural programming statements
      if-else, case
    Procedural assignment statements
      using of = sign

## Slide 7: Mixed Logic
The full digital logic story has been hidden from you up to now
“No one really understands mixed logic”
Hardest thing to understand in digital design
You can get away without knowing it, but good digital designers know it

## Slide 8: Different Circuits?

## Slide 9: Mixed Logic
Based on which “state” causes an action
  ‘1’ action state: positive logic
  ‘0’ action state: negative logic
You’ve already worked with mixed logic

## Slide 10: The Mixed Logic Problem
Implementing the “correct” functions in a mixed logic environment
  Gates are stupid: the react to 1’s and 0’s without knowing about logic levels
The solution: understand logic functions at the basic level
  Approach: match logic levels (bubble matching)

## Slide 11: Mixed Logic Approach
Try not to use mixed logic…
  But if you have to, you need to keep track of the logic levels
Use special indicators
  Positive Logic Convention (PLC)
  Direct Polarity Indicators (DPI)

## Slide 12: Important Vernacular
“Asserted”
  Not necessarily ‘1’ or ‘0’
Positive Logic
  assertation level = high
  asserted high
  Active high
Negative logic
  assertation level = low
  asserted low
  Active low
Is an asserted signal a ‘1’ or ‘0’?
  it depends on logic type

## Slide 13: Approach
Equivalent signals
Equivalent gates

## Slide 14: Equivalent Gates

## Slide 15: Function Forms Revisited
Many different forms of functions
  different forms use different gates
  a few standard ones
  Can be derived from SOP & POS form
Can be written in many ways…
  If your gate is performing an AND function, draw the gate in an AND form
  If your gate is performing an OR function, draw the gate in an OR form

## Slide 16: Good and Bad Implementations
Sad
Happy

## Slide 17: Good and Bad Implementations
Sad
Happy

## Slide 18: The Approach To Mixed Logic
Analysis or Design
Use equivalent gates and equivalent signals where necessary in order to do what you need to do.

## Slide 19: Mixed Logic Analysis Example
What function is being implemented if output is:
  1) Active high
  2) Active low

## Slide 20: Mixed Logic Example
What function is being implemented if output is:
  1) Active high
  2) Active low

## Slide 21: Mixed Logic Example
What function is being implemented if output is:
  1) Active high
  2) Active low

## Slide 22: Mixed Logic Example
Design a circuit that implements the following function:
For this problem consider the A and B inputs and the output as asserted high; all other inputs are negative logic. Implement this function using any type of gates.
F(A,B,C,D) = AD + B

## Slide 23: Experiment 7: Adder/Subtractor
5-bit Adder/Subtractor with validity detection
  Inputs/Outputs are in RC format
  Use foundation modules
Start with block diagram
Provided modules
  8-bit RCA
  sseg_dec.vhd
Simulate
  Submit annotated timing diagram but note testbench VHDL file