## Slide 1: CPE 133
NOR & NAND Latches
D Flip-Flops
Registers

## Slide 2: Lab Issues
Don’t print provided files
Don’t change generic models (n-bit models)
  Override n parameter when instantiated
Don’t forget titles/captions for diagrams
Use courier font only (or equivalent)

## Slide 3: Issues
High-level vs. Low-level
Book chapters
  80% done
  Chapter 20
    Long with low-level details

## Slide 4: New Terminology: Everything you can do with a bit
  Do nothing
    Don’t change value
  Set it
    Make it ‘1’
  Clear it
    Make it ‘0’
  Toggle it (invert it)
    If it’s ‘0’, make ‘1’
    If it’s ‘1’, make it ‘0’

## Slide 5: Two Types of Digital Circuits
Combinatorial Circuits:
  Outputs a function of circuit inputs
  Processes data, but can’t store data (no memory)
  Circuits do not have “state”
Sequential Circuits:
  Outputs a function of the “sequence” of inputs
  Can store data (have memory)
  Have “state” (what’s being memorized)

## Slide 6: Foundation Modules (thus far): all are combinatorial circuits
RCA
Generic Decoder
Standard Decoder
4:1 MUX
Comparator
Parity Generator

## Slide 7: A New Circuit?

## Slide 8: A Seemingly Simple Circuit
td = lumped delay

## Slide 9: Results of Analysis
Full Truth Table
Compressed Truth Table

## Slide 10: Timing Diagram
Significance: circuit can remember one bit
“State”: the value of the bit being remembered

## Slide 11: NOR Latch Models: One Bit Memory
AKA:
Cross Coupled Cell
Cross Coupled NOR Cell
NOR Latch
Latch

## Slide 12: State Diagrams
Common way of modeling sequential circuits
  Shows “important” states of circuit
  What we’ll be doing for remainder of course
Draw state diagram for NOR latch

## Slide 13: State Diagrams

## Slide 14: NAND & NOR Latches
Circuit Form
NAND Latch
NOR Latch
Block Diagram
Excitation Tables

## Slide 15: Verilog MUX Models
module mux_4t1_a(SEL, D, F);
input [1:0] SEL;
input [3:0] D;
output reg F;
always @(SEL, D)
begin
if (SEL == 0) F = D[0];
else if (SEL == 1) F = D[1];
else if (SEL == 2) F = D[2];
else if (SEL == 3) F = D[3];
else F = 0;
end
endmodule
module mux_4t1_a(SEL, D, F);
input [1:0] SEL;
input [3:0] D;
output reg F;
always @(SEL, D)
begin
if (SEL == 0) F = D[0];
else if (SEL == 1) F = D[1];
else if (SEL == 2) F = D[2];
else if (SEL == 3) F = D[3];
end
endmodule
What’s the difference?

## Slide 16: Verilog MUX Models
module mux_4t1_a(SEL, D, F);
input [1:0] SEL;
input [3:0] D;
output reg F;
always @(SEL, D)
begin
if (SEL == 0) F = D[0];
else if (SEL == 1) F = D[1];
else if (SEL == 2) F = D[2];
else if (SEL == 3) F = D[3];
else F = 0;
end
endmodule
module mux_4t1_a(SEL, D, F);
input [1:0] SEL;
input [3:0] D;
output reg F;
always @(SEL, D)
begin
if (SEL == 0) F = D[0];
else if (SEL == 1) F = D[1];
else if (SEL == 2) F = D[2];
else if (SEL == 3) F = D[3];
end
endmodule
If you don’t include a catchall, the synthesizer generates a latch!
Your circuit is “bigger” than it needs to be and probably wont’ work properly

## Slide 17: Flip-Flops
Flip-flop: one-bit storage element
Flip-flop flavors
  D Flip-flop (T Flip-flop, JK Flip-flop)
Sensitivity: when the output can change
  Latch: level-sensitive 1-bit storage element
    Output changes any time inputs change
    Asynchronous circuit
  Flip-flop: edge sensitive 1-bit storage element
    Output can only change on “clock edge”
    Synchronous circuit

## Slide 18: D Flip-flop
Synchronous circuit
  Has clock input
  Output changes are synchronized to active clock edge
“Edge Trigger”
  Rising edge (RET)
  Falling edge (FET)
Internal circuitry: very complicated
  We model at higher-level
Features
  “data” input
  clock input
  complementary outputs

## Slide 19: D Flip-flop
D flip-flop: “Data” flip-flop
The D input of the flip-flop appears on the Q output when the active clock edge occurs
Generate state diagram
Block Diagram
Characteristic Equation
Excitation Table

## Slide 20: D Flip-flop Low-Level Details

## Slide 21: D Flip-flop Timing Diagram

## Slide 22: Summary of Important Stuff
Digital circuit types
  Combinatorial (no memory, no state)
  Sequential (memory & state)
1-bit storage elements
  Latch (level sensitive)
    NOR & NAND latches
  D flip-flop (edge sensitive)
Latch vernacular
  Noun: a 1-bit storage element (or storage elements)
  Verb: to store data in a memory element
Verilog
  Use catchalls to avoid latches in combinatorial circuits