## Slide 1: CPE 133
Review
Register
Verilog Sequential Circuit Models

## Slide 2: Important Items
Everything you can do with a bit
  Set, clear, toggle, nothing
Combinatorial Circuits:
  outputs strictly a function of circuit inputs
  no memory, (thus no state)
Sequential Circuits:
  Outputs are a function of the “sequence” of inputs
  Have memory (thus has state)
Modeling combinatorial circuits with Verilog
  Must a catch-all statement

## Slide 3: State Diagrams
Common way of modeling sequential circuits
  Shows “important” states of circuit

## Slide 4: NAND & NOR Latches
Circuit Form
NAND Latch
NOR Latch
Block Diagram
Excitation Tables

## Slide 5: D Flip-Flops (D for data)
Flip-flop: one-bit storage element
Sensitivity: when the output can change
  Latch: level-sensitive 1-bit storage element
    Output changes any time
    Asynchronous circuit
  Flip-flop: edge sensitive 1-bit storage element
    Output can only change on “clock edge”
    Synchronous circuit

## Slide 6: D Flip-flop
Synchronous circuit
  Output changes are synchronized to active clock edge
Edge Trigger
  Rising edge (RET)
  Falling edge (FET)
Internal circuitry: very complicated
Circuit latches D input into memory element on active clock edge

## Slide 7: D Flip-flop Timing Diagram
Synchronous: output changes are synchronized to rising clock edge

## Slide 8: Verilog MUX Models
module mux_4t1_a(SEL, D, F);
input [1:0] SEL;
input [3:0] D;
output reg F;
always @(SEL, D)
begin
if (SEL == 0) F = D[0];
else if (SEL == 1) F = D[1];
else if (SEL == 2) F = D[2];
else if (SEL == 3) F = D[3];
else F = 0;
end
endmodule
module mux_4t1_a(SEL, D, F);
input [1:0] SEL;
input [3:0] D;
output reg F;
always @(SEL, D)
begin
if (SEL == 0) F = D[0];
else if (SEL == 1) F = D[1];
else if (SEL == 2) F = D[2];
else if (SEL == 3) F = D[3];
end
endmodule
If you don’t include a catchall, the synthesizer generates a latch!
Your circuit is “bigger” than it needs to be and probably wont’ work properly

## Slide 9: SR Latch Verilog Model
---------------------------------------------
-- Model of an NOR-based SR Latch
---------------------------------------------
module sr_latch(S, R, Q);
input S, R;
output reg Q;
always @ (S, R)
begin
if (S == 0 && R == 1)
Q <= 1'b0;
else if (S == 1 && R == 0)
Q <= 1'b1;
end
endmodule
Note: there is no “catch-all”

## Slide 10: Complete D Flip-flop model
module d_ff(D, CLK, Q);
input D, CLK;
output reg Q;
always @ (posedge CLK)
begin
Q <= D;
end
endmodule
posedge in sensitivity list: instructs the synthesize to induce memory
“<=“ indicates non-blocking assignment

## Slide 11
D FF with “other” control inputs as
Can have set and/or reset inputs
  Not necessarily synchronous
    R (reset) is asynchronous

## Slide 12: D Flip-flop with asynchronous Clear
module d_ff_nclr_async(D, CLK, Q, CLR);
input D, CLK, CLR;
output reg Q;
always @ (negedge CLR, posedge CLK)
begin
if (CLR == 0)
Q <= 1'b0;
else
Q <= D;
end
endmodule

## Slide 13: Blocking vs. Non Blocking Assignment
module d_ff_blocking(D,CLK,Q1,Q2);
input D, CLK;
output reg Q1, Q2;
//- blocking assignment
always @ (posedge CLK)
begin
Q1 = D;
Q2 = Q1;
end
endmodule
module d_ff_non_blocking(D,CLK,Q1,Q2);
input D, CLK;
output reg Q1, Q2;
//- non-blocking assignment
always @ (posedge CLK)
begin
Q1 <= D;
Q2 <= Q1;
end
endmodule
Synthesized circuits

## Slide 14: Generic Register: n-bit Storage Element
Block Diagram
Underlying Circuit Diagram

## Slide 15: Register with Load Control
Block Diagram
Timing Diagram Example

## Slide 16: D Flip-flop with asynchronous Clear
module reg_nb(data_in, clk, clr, ld., data_out);
input [n-1:0] data_in;
input clk, clr, ld;
output reg [n-1:0] data_out;
parameter n = 8;
always @(posedge clr, posedge clk)
begin
if (clr == 1) // asynch clr
data_out <= 0;
else if (ld == 1)
data_out <= data_in;
end
endmodule

## Slide 17
Digital Design Foundation Model
Generic Register
Data: DATA_IN: data to be loaded into register
Data: DATA_OUT: Data currently stored by register
Control: CLR: make register store all zeros
Control: LD: must be asserted to store DATA_IN to register
Control: CLK: synchronizes most register operations

## Slide 18: Summary of Important Stuff
Use of posedge and/or negedge in sensitivity list causes synthesizer create a sequential circuit
Two types of procedural assignment statements (statements used inside of always blocks)
  blocking & non-blocking
Use blocking statement for combinatorial circuits
Use non-blocking statements for sequential circuits

## Slide 19: Verilog MUX Models
module mux_4t1_a(SEL, D, F);
input [1:0] SEL;
input [3:0] D;
output reg F;
always @(SEL, D)
begin
if (SEL == 0) F = D[0];
else if (SEL == 1) F = D[1];
else if (SEL == 2) F = D[2];
else if (SEL == 3) F = D[3];
else F = 0;
end
endmodule
module d_ff_nclr_async(D, CLK, Q, CLR);
input D, CLK, CLR;
output reg Q;
always @ (negedge CLR, posedge CLK)
begin
if (CLR == 0)
Q <= 1'b0;
else
Q <= D;
end
endmodule
Combinatorial: blocking
Sequential: non-blocking