## Slide 1: CPE 133 Lecture 15
Review
Finite State Machine Introduction
Counter Introduction

## Slide 2: Summary of Important Stuff
Digital circuit types
  Combinatorial (no memory, no state)
  Sequential (memory & state)
1-bit storage elements
  Latch (level sensitive, asynchronous)
  D flip-flop (edge sensitive, synchronous)
Latch vernacular
  Noun: a 1-bit storage element
  Verb: to store data in a memory element
Registers
  Multi-bit storage elements (synchronous)

## Slide 3: Verilog Modeling Overview
Combinatorial circuits
  Sensitive to signal levels
  Include all signals in sensitivity list
  Include a catchall statement
    Prevents latch generation
  Use only blocking assignment statements
Sequential circuits
  Sensitive to signal edges
  Use posedge & negedge in sensitivity list
    Automatically includes all signals inputs
  Use only non-blocking assignment statements

## Slide 4: Verilog Procedural Assignment Statements
module mux_4t1_a(SEL, D, F);
input [1:0] SEL;
input [3:0] D;
output reg F;
always @(SEL, D)
begin
if (SEL == 0) F = D[0];
else if (SEL == 1) F = D[1];
else if (SEL == 2) F = D[2];
else if (SEL == 3) F = D[3];
else F = 0;
end
endmodule
module d_ff_nclr_async(D, CLK, Q, CLR);
input D, CLK, CLR;
output reg Q;
always @ (negedge CLR, posedge CLK)
begin
if (CLR == 0)
Q <= 1'b0;
else
Q <= D;
end
endmodule
Combinatorial: blocking,
Level-based sensitivity
Sequential: non-blocking,
edge-based sensitivity

## Slide 5
Digital Design Foundation Model
Generic Register
Data: DATA_IN: data to be loaded into register
Data: DATA_OUT: Data currently stored by register
Control: CLR: make register store all zeros
Control: LD: must be asserted to store DATA_IN to register
Control: CLK: synchronizes most register operations

## Slide 6: n-bit Register with asynchronous active high clear
module reg_nb(data_in, clk, clr, ld, data_out);
input [n-1:0] data_in;
input clk, clr, ld;
output reg [n-1:0] data_out;
parameter n = 8;
always @(posedge clr, posedge clk)
begin
if (clr == 1) // asynch clr
data_out <= 0;
else if (ld == 1)
data_out <= data_in;
end
endmodule
clr has precedence over ld

## Slide 7: n-bit Register with synchronous active high clear
module reg_nb(data_in, clk, clr, ld, data_out);
input [n-1:0] data_in;
input clk, clr, ld;
output reg [n-1:0] data_out;
parameter n = 8;
always @(posedge clk)
begin
if (clr == 1) // asynch clr
data_out <= 0;
else if (ld == 1)
data_out <= data_in;
end
endmodule
clr has precedence over ld

## Slide 8: State Diagrams
Great method to model sequential circuits
  Works great for humans
  Presents information more intuitively than PS/NS tables (tabular format)
  Used on many engineering fields
    Computer science as well
The approach:
  Informal & intuitive descriptions now
  More details later

## Slide 9: D Flip-Flop Models
D flip-flop BBD
D flip-flop State Diagram

## Slide 10: D Flip-flop with asynchronous Clear
module d_ff_nclr_async(D, CLK, Q, R);
input D, CLK, R;
output reg Q;
always @ (negedge R, posedge CLK)
begin
if (R == 0)
Q <= 0;
else
Q <= D;
end
endmodule
module d_ff(D, CLK, Q);
input D, CLK;
output reg Q;
always @ (posedge CLK)
begin
Q <= D;
end
endmodule

## Slide 11: D Flip-Flop Models
D flip-flop BBD
D flip-flop with
asynchronous reset

## Slide 12: Finite State Machines (FSMs)
Primarily used as controller circuits
  FSMs as counters good for learning
  Nicely modeled with state diagrams
  Counter: device that outputs a repeatable sequence of numbers (the count)

## Slide 13: FRDDFM Chapter 23
Intuitive approach to state machines
  Builds upon circuits you already know
A “good” chapter
  A unique approach
  Spend some time on the examples

## Slide 14: Design Example #1
Using the diagram below, design a FSM that implements a 2-bit binary counter. The counter’s increments are synchronized with the rising-edge of the CLK input. This counter counts endlessly using this sequence in binary: …0,1,2,3,0,1,…
Provide a circuit diagram
Provide a state diagram

## Slide 15: Timing Diagram: Example #1

## Slide 16: Design Example #4
Using the diagram on the right, design a FSM that implements a synchronous (RET) 2-bit binary up counter. This counter counts up when the CE (count enable) input is a ‘1’ and holds the previous count when the CE signal is ‘0’. Provide both a circuit diagram and state diagram for your solution.
Provide a circuit diagram
Provide a state diagram

## Slide 17: Timing Diagram: Example #4

## Slide 18: Design Example #7
Using the diagram on the right, design a FSM that implements a synchronous 3-bit stoneage binary up counter. The counter also has a positive logic control enable (CE) input that allows the counter to count. Assume the counter increments on the rising clock edge.
Use more than two bits of storage in your FSM
Provide a circuit diagram
Provide a state diagram

## Slide 19: Timing Diagram: Example #7

## Slide 20: General FSM Model

## Slide 21: Experiment #8: Basic FSM Design: Multi- Output 4-Bit Up/Down Counter
Four-bit counter
  Count sequence: {0,1,2… 14,15,0,1,…}
Inputs:
  UP: UP=‘1’ counts up; UP=‘0’ counts down
  CLK
Outputs:
  15-bit stoneage binary
    Use 15 LEDs
  2-Digit decimal count
    Use univ_sseg.v module

## Slide 22: Experiment #8
Yes… big decoders (32 rows)
  Reuse in next experiment
Follow general FSM model
  Use registers, not flip-flops
Clock Divider
  On Polylearn (you must modify for ≈ 2Hz)