## Slide 1: CPE 133
Review
Clocking Issues
Design Examples

## Slide 2: General FSM Model

## Slide 3: Illegal State Recovery
FSMs can have unused state
  Occurs if # of FSM states is not a power of two
What happens when FSM finds itself in an unused state?
  FSM could “hang”
Counter State Diagram: sequence = …6,0,5,7,3,6,0,5…

## Slide 4: Hang States
What you want
What you might get
How to “fix it”

## Slide 5: Clock Signals
Clocks are generally periodic in nature
  Waveform repeats itself after a constant period of time
  Period = the amount of time it requires for a clock signal to repeat itself
periodic
non-periodic

## Slide 6: Period & Frequency
Period  represented by T
  Units: seconds
Frequency = 1/T (T-1)
  Units: seconds-1 = Hertz = Hz

## Slide 7: Clock Signal Attributes
Duty Cycle
  Percentage of the signal period that the signal is in the high state
unitless

## Slide 8: The State Diagram
Designed for the human viewer
  looks better than a PS/NS table
Convey four types of information
  states in the FSM
  state transitions
  inputs conditions (control the state transitions)
  outputs
    Moore (function of state)
    Mealy (function of state and external inputs)

## Slide 9: The State Bubble
Bubble represents a state
  has a self-commenting name
  defined by values in underlying storage elements
states are have temporal delineation
  Most state changes are synchronized with clock edge
    There as also asynchronous transfers
Present state? Next state?
Rising Edge Triggered Storage Elements

## Slide 10: The State Diagram
Used to indicate “everything”
  Changes in state
  Conditions that cause state changes (external inputs)
  Values of external outputs
Two types of state transitions
  Self-loops
  Transition to another state

## Slide 11: Controlling the Transitions
Transitions based on:
    current state
    current value of external inputs
  Always list conditions that allow transition to occur
  Unconditional transitions indicated with “-”

## Slide 12: Representing Outputs
Moore Outputs
Mealy Outputs

## Slide 13: Representing Outputs
Mealy and Moore outputs

## Slide 14: More FSMs
Primarily used as controller circuits
Also used to make
  Specialty counters
    Sequences other then increment & decrements
  Synthesize signal
    Varying frequency
    Varying duty cycles

## Slide 15: Design Problem #1
Design a circuit that blinks a single LED at half the input clock frequency with a 50% duty cycle. Include a black box diagram (BBD).
Design not using a FSM
  Classic digital design circuit
Design using an FSM
  Provide a state diagram

## Slide 16: Solution

## Slide 17: Design Problem #2
Design a circuit that blinks an LED. If the button is pressed, the LED stops blinking and either stays ON or stays OFF depending on when the button is pressed or not.
Include a black box diagram (BBD)
Include a state diagram

## Slide 18: Solution

## Slide 19: Design Problem #3
Design a circuit that blinks an LED. If the button is pressed, the LED stops blinking and turns off.
Include a black box diagram (BBD)
Include a state diagram

## Slide 20: Solution

## Slide 21: Design Problem #4
Design a circuit that blinks an LED with a 33.3% duty cycle at 60MHz.
Include a black box diagram (BBD)
Include a state diagram
Show the FSM clock frequency to obtain the 60MHz circuit specification

## Slide 22: Solution

## Slide 23: Design Problem #5
Design a circuit that blinks an LED with a 50% duty cycle if a button is pressed; otherwise the LED blinks with a 25% duty cycle. It’s OK for one duty cycle to be off in some cases where the button changes state.
Include a black box diagram (BBD)
Include a state diagram