## Slide 1: CPE 133: Lecture 19
FSM Review
Verilog Behavioral FSM Models
Experiment #10

## Slide 2: Timing Diagram
Moore
Mealy

## Slide 3: FSM Modeling with Verilog
Generic FSM Model
Verilog FSM Model

## Slide 4: The Verilog FSM Template
Many ways to do model FSM in Verilog
  Pick one; stick with it
FSM Modeling in Verilog
  Not engineering, total grunt work
  Only looks intimidating for a few minutes
Know where to find copy of template
  Don’t do start Verilog FSM model from scratch

## Slide 5: Verilog FSM Template: Interface
Black Box Diagram
Verilog interface code
module fsm_template(reset_n, x_in, clk, mealy, moore);
input reset_n,
input x_in,
input clk;
output reg mealy;
output reg moore;

## Slide 6: Verilog FSM Template: State Specification
State specification
//- next state & present state variables
reg [1:0] NS, PS;
//- bit-level state representations
parameter [1:0] st_A=2'b00, st_B=2'b01, st_C=2'b11;
Provide NS & PS declarations
  As reg (assigned in states)
Provide bit values for each state
  Each state must have unique values

## Slide 7: Verilog FSM Template: Sequential Block
State register model
//- model the state registers
always @ (negedge reset_n, posedge clk)
if (reset_n == 0)
PS <= st_A;
else
PS <= NS;
Assigns PS
  Memory associated with PS
  Sequential module, non-blocking assignment used
  Sequential statements, so asynchronous signal has precedence

## Slide 8
State Diagram
always @ (x_in,PS)
begin
mealy = 0; moore = 0; //- assign all outputs
case(PS)
st_A: //--------------------------------
begin
moore = 1;
if (x_in == 1)
begin
mealy = 0; NS = st_A;
end
else
begin
mealy = 1; NS = st_B;
end
end
st_B: //--------------------------------
begin
moore = 0; mealy = 1; NS = st_C;
end
st_C: //--------------------------------
begin
moore = 1;
if (x_in == 1)
begin
mealy = 1; NS = st_B;
end
else
begin
mealy = 0; NS = st_A;
end
end
default: NS = st_A; //- catchall
endcase
end

## Slide 9: Exp #10: 3-Bit Up/Down Counter
Counter with multiple control inputs
Implement FSM with Verilog behavioral model
  Asynchronous signals go in sequential process
  Synchronous signals go in combinatorial process
Output display:
  Use seven-seg decoder or univ_sseg.v
  Choose any buttons/switches you want
Top-level BBD Exp #10

## Slide 10: Experiment #10 Tips
Big FSM, lots of repetition
Be clever with combinatorial procedural block
  Code in procedural blocks is sequential
    If HOLD = 1 then don’t change state
    If the previous statement does not test true, you know HOLD must be ‘0’; you don’t need to check that condition in later if clauses
  Nested if’s with simple conditions are better than non-nested if’s with complex conditions

## Slide 11: Design Problem #5 (from previous)
Design a circuit that blinks an LED with a 50% duty cycle if a button is pressed; otherwise the LED blinks with a 25% duty cycle. It’s OK for one duty cycle to be off in some cases where the button changes state.
Include a black box diagram (BBD)
Include a state diagram