## Slide 1: CPE 133
FSMs as Controllers
Counters
Example Problems
Experiment 12

## Slide 2: FSM as a Controller
External inputs (status)
External outputs (control)

## Slide 3: Foundation Notation

## Slide 4: Foundation Modules (thus far)
RCA
Generic Decoder
Standard Decoder
4:1 MUX
Comparator
Parity Generator
Register

## Slide 5: Counter: a Register with Features

## Slide 6: Typical Counter Lingo
Count sequence
N-bit counter
Up, down, up/down counter
Increment, decrement, hold
Overflow, underflow
Circular
Cascadeable
Parallel load

## Slide 7: Foundation Module: Counter

## Slide 8: Example
Use the BBD to complete the timing diagram below:
  UP allows the counter to increment when asserted and decrement when not asserted.
  RCO indicates the counter is outputting its terminal count.
  LD has precedence over HOLD and UP
  HOLD had precedence over UP

## Slide 9: Solution

## Slide 10: Verilog Generic n-Bit Counter
module cntr_udclr_nb(clk, clr, up, ld, D, count, rco);
input clk, clr, up, ld;
input [n-1:0] D;
output reg [n-1:0] count;
output reg rco;
parameter n = 8;
always @(posedge clr, posedge clk)
begin
if (clr == 1) // asynch reset
count <= 0;
else if (ld == 1) // load new value
count <= D;
else if (up == 1) // count up (increment)
count <= count + 1;
else if (up == 0) // count down (decrement)
count <= count - 1;
end
always @(count, up) // direction dependent RCO
begin
if ( up == 1 && &count == 1'b1)
rco = 1'b1;
else if (up == 0 && |count == 1'b1)
rco = 1'b1;
else
rco = 1'b0;
end
endmodule
n-bit up/down counter with asynchronous RESET

## Slide 11: Counter Module Usage Options
Use what you need, but:
Always clearly state your assumptions because unlike HDL models, the BBD reader won’t know your intentions

## Slide 12: Design Problem #1
Design a circuit with the following count sequence is: (6,7,8,9,10,11,12, 13, 14, 15, 6,7,8,9,10...) This circuit also has an extra LED output that is on when the counter output is greater than 11.
  Show top two levels for BBDs
  Annotate schematic as necessary
  State how the circuit is controlled

## Slide 13: Timing Diagram

## Slide 14: Design Problem #2
Design a circuit with the following binary count sequences: the count sequence is either (3→15) or (6→15) based on whether a button is pressed or not, respectively. This counter has an extra LED output that indicates when the count is less than 8.
  Show top two levels for BBDs
  Annotate schematic as necessary
  State how the circuit is controlled

## Slide 15: Design Problem #3
Design a circuit that drives four LEDs with a binary count. The circuit only counts up. The circuit also has an extra LED output that turns on for one [0,15] count, then off for the next [0-15] count, etc.
  Use no more than a single 4-bit counter
  Show top two levels for BBDs
  Annotate schematic as necessary
  State how the circuit is controlled

## Slide 16: Design Problem #4
Design a circuit that outputs the following sequence:
(…14,15,0,0,0,1,2,3,4,5,6,7,8,9,19,11,12,13,14,15,0,0,0,1,2…)
  Show top two levels for BBDs
  Annotate schematic as necessary
  State how the circuit is controlled

## Slide 17: Design Problem #5
Design a circuit that has four 8-bit unsigned binary inputs. Upon a button press, the circuit finds and displays the maximum value of the four inputs
  Assume inputs don’t change “too fast”
  Result persistent until next until button press.
  Use only one comparator in your design
  Verify the button release before new search
  State how the circuit is controlled

## Slide 18: Experiment #12
Design a circuit that sorts four 4-bit unsigned values (from 16 switches) and displays the results on the 7-segment display.
  Bubble sort is intuitive and straightforward
  Sort starts with the press of a button,
    Results persistent until next button press
  Use less than 14 modules in your design
  Write your own display multiplexor
    Reuse from Exp 9