## Slide 1: CPE 133
Accumulators & Event Counters
Shift Registers
Example Problems
Experiment #13

## Slide 2: Accumulators
Adds list of numbers
  You can only add two items at a time
    Adds current value to running total
  You must properly specify sum bit-width

## Slide 3: Event Counters
Special case of accumulator
  If you’re always accumulating a ‘1’, use the incrementing feature of a counter (UP)
Could be useful in a parity checking circuit…

## Slide 4: Shift Registers
Shift Registers
  Special case of registers
  Massively useful (Do Examples)
    Fast binary multiplication
    Fast binary division

## Slide 5: Shift Register: General Case
N-bit shift register
Features
  All 1-bit registers share same clock
  n-bits of data shift right simultaneously
  Left-most bit input from “outside world”
  Right-most bit shifts out to “somewhere”

## Slide 6: 4-Bit Shift Register Example

## Slide 7: 3-Bit Shift Register (right)
Sample Timing Diagram: 3-bit Shift Register

## Slide 8: Foundation Module Notation
For provided USR Module, x=2

## Slide 9
module usr_nb(data_in, dbit, sel, clk, clr, data_out);
input [n-1:0] data_in;
input dbit, clk, clr;
input [1:0] sel;
output reg [n-1:0] data_out;
parameter n = 8;
always @(posedge clr, posedge clk)
begin
if (clr == 1) // asynch reset
data_out <= 0;
else
case (sel)
0: data_out <= data_out; //- hold value
1: data_out <= data_in; //- load
2: data_out <= {data_out[n-2:0],dbit}; //- shift left
3: data_out <= {dbit,data_out[n-1:1]}; //- shift right
default data_out <= 0;
endcase
end
endmodule

## Slide 10: Design Problem #1:
Design a circuit that upon a button press, divides an 8-bit unsigned binary input values by two for as many times as required to make the result of the input value less than 17. The result of this operation is also an 8-bit unsigned binary number.
  Consider the output persistent
  Show a BBD of your solution
  Minimize hardware in your solution
  State what type of control the circuit has

## Slide 11: Design Problem #2:
Design a circuit that outputs a value 5.5 times greater than the input value upon the pressing of a button.
  Assume the input “stays around” for awhile
  Assume the input is an 8-bit unsigned binary value and the width of the output is minimized but the answer is valid and persistent.
  Show a BBD of your solution
  Minimize hardware in your solution (use no more than one RCA in your design)
  State what type of control the circuit has

## Slide 12: Experiment 13: Serial Parity Generator
Upon button press, circuit calculates parity associated with 16 dev board switches
Display
  Two 7-seg digits: “EE” or “oo” (even & odd parity)
  Two 7-seg digits: count of switches that are “on”
Use FSM in design
Use display multiplexor from Exp 12 (with mods)