## Slide 1: CPE 133
Foundation Modeling Design Overview
Experiment 14
Example Problems

## Slide 2: Foundation Modules
RCA
Generic Decoder
Standard Decoder
4:1 MUX
Comparator
Register
Counter
Shift Register

## Slide 3: Design Problems/Solutions: Mathematical Operations
Operation | Hardware
Accumulate List of numbers | 
Number of events | 
Addition/Subtraction | 
Multiplication | 
By 2n | 
By any number | 
Division | 
By 2n | 
By any number | 

## Slide 4: Design Problems/Solutions: Mathematical Operations
Operation | Hardware
Accumulate List of numbers | Accumulator (RCA & Register)
Number of events | Counter
Addition/Subtraction | RCA
Multiplication | 
By 2n | Shift Register (shift left)
By any number | Repeated addition (accumulator)
Division | 
By 2n | Shift Register (shift right)
By any number | Repeated subtraction (accumulator)

## Slide 5: Design Problems/Solutions: Miscellaneous Operations
Operation | Hardware
Delays (do same thing for awhile) | 
Fixed delay (a few) | 
Fixed delay (many) | 
Event controlled | 
Logic | 
Simple | 
Complex | 
Decision (select one of several) | 

## Slide 6: Design Problems/Solutions: Miscellaneous Operations
Operation | Hardware
Delays (do same thing for awhile) | 
Fixed delay (a few) | FSM states
Fixed delay (many) | Counter with RCO
Event controlled | FSM self-loop
Logic | 
Simple | Gates
Complex | Decoder (LUT)
Decision (select one of several) | MUX

## Slide 7: Design Problems/Solutions: More Miscellaneous Operations
Operation | Hardware
Comparisons General Without Comparator Greater than? Less than? | 
Bit Operations Odd/Even Negative/Positive Evenly divisible by 2^n | 

## Slide 8: Design Problems/Solutions: More Miscellaneous Operations
Operation | Hardware
Comparisons General Without Comparator Greater than? Less than? | Comparator Are upper bits set? Are upper bits cleared?
Bit Operations Odd/Even neg/pos Evenly divisible by 2^n | LSB set/cleared Sign bit set/cleared Lower n-bits cleared

## Slide 9: Experiment #14 FSM Based 5-Bit Multiplier
Multiplication by adding/shifting
3-bit multiply example:

## Slide 10: Experiment #14 FSM Based 5-Bit Multiplier
Design cries out for registers
  Simple registers to store values
  “accumulator” to store running result total
  Shift register for “shifting”
Also
  Use univ_sseg.v for output
  Use clock divider to view operation
  Use one LED per state for debugging (maybe)

## Slide 11: Design Problem #1:
Provide a state diagram that models a 2-bit right shifting shift register.
  The shift register has one data input D
  The shift register has a H input (hold) that prevents the circuit from changing state when asserted.
  The shift register has an asynchronous RESET input that puts the shift register to the “00” state.
  Input precedence (hi to low): RESET, H

## Slide 12: Design Problem #2:
Provide a state diagram that models a 2-bit shift register.
  The shift register has one data input D
  The shift register has a R input that causes a right shift when asserted or a left shift if not asserted.
  The shift register has a H input (hold) that prevents the circuit from changing state when asserted.
  The shift register has an asynchronous RESET input that puts the shift register to the “00” state.
  Input precedence (hi to low): RESET, H, R

## Slide 13: Design Problem #3:
Design a circuit that upon a button press, accumulates the 8-bit unsigned binary input. Each clock cycle, it potentially adds the input to the running total. The circuit continues to operate until a the accumulated value exceeds the 8-bit output, at which time it stops, displays the total, and waits for another button press.
  The input value that exceeds the 8-bit output is not added to the circuit.
  Show a BBD supporting your solution.
  Use an FSM in your design and provide a state diagram modeling that FSM
  State how the circuit is controlled