## Slide 1: CPE 133
Administrative Stuff
Foundation Module Review
Example

## Slide 2: Administrative Stuff
Experiments 12-14 need to be demo’d to me
  I plan on perusing your Verilog models
Final Exam materials posted
  Cheatsheets
    Use the same cheatseets for both finals
  Study guide
    It’s negotiable; take a look
  Old Exams
    Only Spring 2018 is posted
    Others are mostly meaningless

## Slide 3: RCAs
Input/Output
Data In: A, B, Cin. A & B are addends; Cin is the carry in.
Control In: none
Data Out: SUM. Summation of: A+B+Cin.
Status Out: Co. The Carry out; indicates if the RCA’s addition operation generated a carry out of the module’s MSB.
Usage
Use for addition or subtraction
A primary component of accumulators
The RCA’s carry out (CO) is effectively the (n+1)th bit of a n-bit addition
Indicates “validity” of SUM output when using unsigned binary

## Slide 4: MUXes
Input/Output
DATA IN: A, B, C, etc;
CONTROL: SEL; selects which data input appears on DATA OUT; width of SEL signal is such that 2SEL ≥ the number of data inputs.
DATA OUT: A single output, which is one of the inputs
STATUS: none
Usage
use for decisions
the hardware approach to decisions is to generate values for all MUX inputs and then select one as output
The width of the data inputs and data outputs generally match

## Slide 5: Comparators
Input/Output
DATA IN: A, B. the two bundled values to be compared.
CONTROL: none
DATA OUT:: none
STATUS: EQ (A=B), LT (A<B), GT (A>B)
Usage
Circuits use comparators when they need to establish equality relationships between two numbers
The data width of the two inputs is generally the same
When appearing in circuits, comparators don’t need to include every status output

## Slide 6: Generic Decoders
Input/Output
DATA IN: DATA; the function’s independent variables
CONTROL: none
DATA OUT: DATA; the function’s dependent variables
STATUS: none
Usage
Circuits use decoders:
  as LUTs where we have pre-calculated values (DATA OUT) indexed by DATA IN
  as replacement for complex logic
You must include an adequate description of a generic decoder if you use it in a circuit

## Slide 7: Standard Decoders
Input/Output
DATA IN: none.
CONTROL: SEL; selects the form of the output
DATA OUT: none
STATUS: Sx; the set of outputs in one-hot or one-cold form
Usage
Circuits use standard decoders when they need to select only one of several outputs to actuate
Standard decoders are a subset of generic decoders

## Slide 8: Parity Generators
Input/Output
DATA IN: data used for establishing parity
CONTROL: none
DATA OUT: none
STATUS: PAR bit provides information regarding the parity of the DATA IN bits
Usage
Use parity generators to:
  Check the parity o f the DATA IN bits
  Generate a given parity of the input DATA_IN bits plus a parity bit(DATA IN & PAR) is of a given parity
The notion of parity is also associated with a serial bit stream

## Slide 9: Registers
Input/Output
DATA IN: data to synchronously load into register.
CONTROL: CLK, LD, CLR; The CLK signal synchronizes the data loading, which happens when both an active clock edge and asserted LD; CLR input clears each bit storage element in the register
DATA OUT: data in register
STATUS: none
Usage
Circuits use registers when they need to store values
Register loading is always synchronous, while clear-type inputs can be either asynchronous of synchronous
Primary component of an accumulator

## Slide 10: Counters
Input/Output
DATA IN: data for sync load
CONTROL: CLK, LD, CLR, UP, DOWN, HOLD. CLK syncs data load and counter changes; counts up or down or holds; LD signal controls data loading; CLR input clears register storage
DATA OUT: OUT_DATA; the data stored in circuit
STATUS: RCO establishes when the counter outputs are at the counter’s terminal value (direction dependent)
Usage
use counters in two ways:
  Track # of times something happened (event counter)
  to make circuit do some action a given number of times
UP, DOWN, & HOLD functionality is flexible (must specify)
RCO is direction dependent
OK not to use all inputs & outputs

## Slide 11: Shift Registers
Input/Output
DATA IN: data to load into shift register; DBIT becomes the new left or right-most bit of register
CONTROL: CLK, LD, CLR, SEL. SEL selects the USR functionality such as hold, load, shift-left, and shift-right functionality, synched with the CLK
DATA OUT: data stored in the shift register.
STATUS: none
Usage
use when circuit requires
  fast division by two (right shift) or fast multiplication by two (left shift)
  when they requires special shift-type bit manipulation (rotates, arithmetic shifts, etc.)

## Slide 12: Example Problem
Design a circuit that upon receiving a GO signal, counts and displays the number of times the same 8-bit value appears on the inputs for three consecutive clock cycles. The circuit continues checking for the three values for 1024 clock cycles (appearing on an active clock edge). The circuit’s output is persistent until another GO signal is received. Assume the circuit receives one value per clock signal.
  xMinimize the use of hardware in your design
  Provide a state diagram if you use a FSM
  State how your circuit is contolled