## Slide 1: CPE 133
Admin Stuff
Review
Example Problem

## Slide 2: Admin Stuff
Cheatsheet contents are negotiable
  Not study guide (as previously stated)
All scores are posted
  Let me know if something is incorrect
  Quiz scores
    Still missing some quiz 7 scores?
  Experiments
    Only posted through Exp 11

## Slide 3: Important Stuff
Validity of math operation (add or sub)
  Always involved when using a RCA
    Is the SUM output valid?
Signed numbers (RC format)
  Check sign bits of A & B operands, & SUM
Unsigned numbers
  Check CO (carry out)

## Slide 4: Example Problem
Design a circuit that upon receiving a GO signal, turns on the circuit’s single LED output. The circuit first looks for 8 values of 0x53 on the circuit’s 8-bit input on the circuit’s active clock edge. When it finds the eight value, it searches for 8 more values of 0x47. When it finds those sets of 8 values, it turns on the LED and waits for another GO signal. The circuit searches for no more than 1024 times per GO signal; if it does not find them, the circuit turns off the LED. Include a RESET input that puts the circuit into a known (with the LED off).
  Provide top two levels of BBD
  Minimize the use of hardware in your design
  Provide a state diagram if you use a FSM
  Use no more than one comparator in your design